## Slide 1
ITU AI/ML 5G Challenge
Theme 1 from KDDI
Analysis on route information failure in IP core networks by NFV-based test environment
UT-NakaoLab-AI Team 2020-10-15
Team Members: Fei Xia (M1), Aerman Tuerxun (M1), Jiaxing Lu (D1), Ping Du

## Slide 2
Background
Network failure and anomaly detection is desired to be automatically performed by AI/ML for operating 5G mobile networks.
Challenges in AI/ML
  How to extract features from the huge amount of unstructured log files collected from network routers and devices.
  How to identify important features to reduce the computation.
  How to detect failures with a small amount of data in real-time.
2

## Slide 3
Summary
First, we extract features from huge amount of log files into 997 features.
Then, we refine features to with differential data to highlight the difference between normal and abnormal data.
Third, we identify the most important 30 features so that we can reduce computation without degrading the performance.
Moreover, our work extended KDDI’s NOMS2020 paper as follows:
  Our model can target 7 failure cases while the NOMS2020 paper address only 3 failure cases.
  We can use use one unified model to predict both device and interface errors, while NOMS2020 paper use different models to predict network and network failures separately.
  Besides the Multiple-layer perceptron (MLP), Random Forest (RF), and Support Vector Machine (SVM) machine learning algorithms, we also add Decision Tree (DT) and XGBoost (XGB) to the comparative analysis.

## Slide 4
Feature Reduction
Model Training
Agenda
Model Evaluation
02
01
02
Feature Extraction
Feature Refinement
03
05
04

## Slide 5
01
PART ONE
Feature Extraction

## Slide 6
Extract features from Log files (JSON format) and merged features with label based on time it into CSV files
Physical File
Virtual File
Network File
Log files
(14 Types of Events)
Label files
Physical CSV
Virtual CSV
Network CSV
CSV files
Merge based on time
Feature Extraction

## Slide 7
Feature Extraction
Key Points in Feature Extraction
For all log files, we utilize path like “key1/key1-1/key1-1-1…” as keys to extract features from physical-infrastructure, virtual-infrastructure, and network-device JSON log files.
For BGP related entries, we use the number of next-hops in each array and their prefixes as features.

## Slide 8
02
PART TWO
Feature Refinement

## Slide 9
To highlight the difference between normal and abnormal data sets to derive metrics which have changed since the occurrence of a failure, we use differential data between the 5th minute data and the 1st minute data as input.
Differentiate Data as Input
Feature Refinement

## Slide 10
Feature Refinement
Physical
Virtual
Network
data-for-learning, CSV format
Merge
CSV
For Training
Physical
Virtual
Network
data-for-evaluation, CSV format
Merge
CSV
For Testing
Merge diverse datasets
learning
evaluation
To train a unified model for diverse network events, we merge all datasets into one csv file for training and testing.

## Slide 11
03
PART THREE
Feature Reduction

## Slide 12
Feature Reduction
Feature Importance Analysis
Importance is calculated for a single decision tree by the amount that each attribute split point improves the performance measure, weighted by the number of observations the node is responsible for.
The performance measure may be the purity used to select the split points or another more specific error function.
The feature importance is then averaged across all of the the decision trees within the model.

## Slide 13
Feature Reduction
Use different numbers of features to train the data and observe the changes in accuracy.
  Through importance analysis of features, we can only use top 30 important features to achieve the same high performance.
Different Features Accuracy

## Slide 14
04
PART FOUR
Model Training

## Slide 15
Model Training
Training & Validation with Learning Data
Training Model
8 : 2
Dataset Files for Learning
Failure Management
Virtual
Physical
Network
Data Pre-process
Training
Validation
No. | Method | Accuracy
1 | XGBoost | 0.77
2 | Radom Forest | 0.76
3 | Decision Tree | 0.73
4 | SVM | 0.58
5 | MLP | 0.54
Validation accuracy during training

## Slide 16
05
PART FIVE
Model Evaluation

## Slide 17
Model Evaluation
Type 1, 3, 9 and 11 are identified very well using most of the models while the accuracies of type 5 (Packet Loss) and 7 (Packet Delay) are very low
Evaluate By Precision
 | All Data |  | 
Label Type | dt | rf | xgb
1: node-down | 0.97 | 1.00 | 1.00
3: interface-down | 0.41 | 0.97 | 0.85
5: tap-loss | 0.45 | 0.56 | 0.54
7: tap-delay | 0.40 | 0.50 | 0.55
9: ixnetwork-bgp-injection | 0.97 | 0.99 | 0.97
11: ixnetwork-bgp-hijacking | 0.84 | 1.00 | 1.00
(True Positive (TP), False Positive (FP) )

## Slide 18
Our comparative analysis confirm the KDDI’s finding that Random Forest (RF) outperforms SVN and MLP algorithms.
We also find that the XGBoost algorithm has a comparable performance as that of RF.
We also found there is still room for improvement for the the failure cases: tap-loss and tap-delay, which are not discussed the NOMS2020 paper. These are left for our future work
Comparative Analysis

## Slide 19
Contributions
First, we introduce our feature extraction mechanism especially for network BGP data
Then, we use differential data as input to highlight features of abnormal data.
Third, we analyze and identify the most important 30 features to reduce computation without degrading the performance.
Comparing to the work in NOMS2020 paper:
  Our model can target all list 7 failure cases while the NOMS2020 paper address only 3 failure cases.
  We use one unified model for all failure cases, while NOMS2020 paper use different models to predict network and network failures separately.
  We also add Decision Tree (DT) and XGBoost (XGB) to the comparative analysis and point out that XGBoost has a comparable performance as Random Forest.

## Slide 20
Thanks
UT-NakaoLab-AI Team 2020-10-15